## Slide 1: Adding OpenCL Support to Vortex GPGPU
Blaise Tine, Fares Elsabbagh

## Slide 2: Open-Source OpenCL Implementations
Name | Version | Targets | Status | URL
Intel Beignet | 2.0 | x86 | Closed | https://cgit.freedesktop.org/beignet
Intel Neo | 2.1 | X86 | Active | https://01.org/compute-runtime
POCL | 1.2 | x86, ARM, AMD, TCE, PTX | Stable | https://github.com/pocl/pocl
ROCm | 1.2 | AMD | Stable | https://github.com/RadeonOpenCompute
TI-OpenCL | 1.1 | TI | Closed | https://git.ti.com/opencl/ti-opencl
Shamrock | 1.2 | TI | Active | https://git.linaro.org/gpgpu/shamrock.git
libclc | 1.2 | AMD, PTX | Closed | https://libclc.llvm.org/
Clover | 1.1 | AMD | Closed | https://people.freedesktop.org/~steckdenis/clover/
There are a few open-source OpenCL implementations
Most of them are vendor driven
Most of them only support vendor specific device targets
Only POCL supports a wider range of device targets

## Slide 3: POCL: A Performance Portable OpenCL Implementation
Key Insights:
  Use target-specific execution model
    SIMT -> GPUs
    MIND, SIMD -> CPUs
  Target-specific compiler transformations
    Using LLVM
Key Features:
  A single interface with multiple target devices
  Support HSAIL export
  Support PTEX export
  Custom accelerator support via TCE*
  Support SPIR import
POCL Software Stack
* TTA-based Co-design Environment - http://openasip.org/

## Slide 4: POCL Software Stack
Host-device Interface
  Routes device-specific function calls
Host Layer
  Interfaces with user application
  Devices query API
  OpenCL runtime implementation
  OpenCL compiler implementation
Device Layer
  Command queue management
  Kernel loading and execution
  Device properties query
  Target-specific kernel compilation passes
  Built-in/hand-optimized routines
* TTA-based Co-design Environment - http://openasip.org/

## Slide 5: POCL Compilation Chain
Input User Program
  OpenCL kernel
    Use Clang to generate LLVM IR
  SPIR program
    Direct conversion to LLVM IR
Kernel Compilation
  Generate single work-item function
  Link target-specific build-in functions (sin, cos, sqrt, etc..)
  Generate work-group function for non-SPMD
  Target-specific optimizations
  Fine-grained parallelization
* TTA-based Co-design Environment - http://openasip.org/

## Slide 6: Vortex Unique Architecture
PC
TM
RegisterFile
PC
TM
RegisterFile
PC
TM
RegisterFile
PC
TM
RegisterFile
I-Cache
D-Cache
Warp
Scheduler
Fetch
Decode
Execute
memory
Writeback
Vortex is a RiscV SIMT processor
  Configurable 1-32 compute nodes (Warps)
  Configurable 1-32 threads per warp
ISA Extension
  Minimal RiscV ISA modification
    Increases portability
  New instructions for Warps/Threads
    wspawn, clone, tmc, split, join, barrier
Execution Model
  In-place execution (no-offloading)
  Use ‘fork’ to partition work across warps/threads
Limitations
  No OS support

## Slide 7: POCL Support for RiscV CPUs
There is currently no official support for RiscV
Adding support for RiscV with limited changes
  Clone the existing ARM backend implementation
  Enable POCL cross-compilation for LLVM-RiscV
  Disable device-specific functions
  Disable device-specific optimizations
Requirements
  Linux environment with pthread library
Limitations
  Offline kernel compilation only
RISCV-V CPU
Offline Compilation
POCL Runtime
Linux Kernel
pthread
POCL Compiler
Kernel
Binary
OpenCLKernel
Kernel
OpenCL Application

## Slide 8: POCL Support for Vortex
NewLib BSP
  A barebone std C++ libraries without OS dependency
  Implement NewLib stub functions for Vortex emulator
    Memory allocator, File IO and console output
POCL Runtime
  Remove linux & pthread dependencies to use NewLib
  Modify kernel compilation to use load from static library
  Modify kernel invocation to use Vortex spawn instr.
  Modify linker to generate runtime as static library
POCL Compiler
  Enable cross-compilation for RiscV CPU targets
  Implement registration API for static kernels (RegLib)
  Cross-compile kernel to static library
Vortex CPU
Offline Compilation
POCL Runtime
NewLib
Vortex Lib
Kernel
OpenCL Application
POCL Compiler
Kernel
Object
OpenCLKernel
GCC Linker
RegLib
Kernel
Kernel
Binary

## Slide 9: POCL Support for Vortex (2)
Kernel Compilation Changes
  Work-group lowering
  Work-item lowering
  Control-flow divergence
Built-in Library Support
  cos, sin, sqrt, etc..
  Native implementations
Unique Codegen Optimizations?
  TDB*
Vortex CPU
Offline Compilation
POCL Runtime
NewLib
Vortex Lib
Kernel
OpenCL Application
POCL Compiler
Kernel
Object
OpenCLKernel
GCC Linker
RegLib
Kernel
Kernel
Binary

## Slide 10: POCL Support for Vortex (3)
Hardware Support for POCL
  Native Barriers Support
    Currently implemented in software
    HW support greatly simplifies codegen
    HW support greatly improves performance
    Design complexity: medium
  Floating-point Extension
    Needed for running OpenCL benchmarks
    Use existing Verilog IP for FP processors
    Need to modify Vortex pipeline
      New floating-point register file
      New floating-point control/status registers
      Floating-point exception handling
      Floating-point to integer conversion
    Design complexity: high

## Slide 11: Work Items Status
Current Status
  Test LLVM support for RiscV
  Test POCL compilation on X86
  Test POCL cross-compilation for ARM
  POCL Cross-compilation for RiscV
  Kernel registration API
  POCL support for NewLib RiscV CPUs
  Vortex emulation update to match RTL
  NewLib Support on Vortex
  POCL running on Vortex
  Test vecadd on Vortex
  Port rodinia benchmark to Vortex